## Slide 1
Train Speed Reset
Train Emergency Stop
Train Sensor
Train Station
Railway Cross Signal
Green: Pass [off]
Red: Block [on]

## Slide 2
Real work sensor data
PCL coil output data
Database
Communication manager
PCL input data
PCL coil output data
ModBus TCP
PLC simulator VM
SCADA HMI data Visualization
Metro Control HMI

## Slide 3
Signal Trigger on sensor
Signal Trigger off sensor
Railway control signal
Use PLC to create a T Flip – Flop latching relay with signal trigger on has high priority

## Slide 4
Railway System Emulator [ Program workflow diagram]
Program start
Loading config files
Program system config file
Station config file
Scenario config file
Init main UI (main thread)
Init PLC request handler (sub thread )
UI data controller (map manager)
Display UI map panel
Train power control panels
Display UI refresh loop
Components state data
Control event
PLC data controller (data manager)
Holding register data
Coil state change data
PLC Connector (UDP server)
PLC state data
Network
Other PLC modules
Other PLC modules
Other PLC modules
Use UDP to simulate the real-word electrical system wires connection
System auto controller ( if test mode )
All Plc connection and data update state

## Slide 5
Train
Scenario load drop down menu
Date and Time
Station
PLC connection state
Trains power control panels
Trains collision auto avoidance control
Train position sensors
Railway track signals

## Slide 6
Train control panel
Train power on Button
Train position reset button
Emergency Stop button (power cut off)
Train auto collision avoidance on/off control
Train auto collision avoidance OFF:
Behind train will “hit” the front stopped train directly and stop. An accident indicator will flash at the accident position
UI scenario :
Train auto collision avoidance ON:
Behind train will change speed to 0 to wait the front train if the train’s sensor detects a train in it front in the safety threshold distance.
UI scenario :
Step 1: click config dropdown menu and select “load scenario”
Step 2:When the Scenario selection window pop-up,
Click the Scenario you want to load
Step 3: Click “OK” to load to the real-world simulator

## Slide 7
Junction entrance block sensor
Junction Area
Junction entrance release sensor
T-flip-flop latching relay implemented by PLC ladder logic
Train entrance block signal
Step 1: When a train is entering the junction and trigger the entrance block sensor (sensor color change from grey to blue )
Operation Scenario 1: Junction block when train pass through
Step 2: Junction entrance block signal will turn on (red) to block the train on yellow track to enter the junction
Operation Scenario 1: Junction release when train leaving
Step 3: When a train is leaving the junction and trigger the entrance release sensor (sensor color change from grey to blue )
Step 4: Junction entrance block signal will turn OFF (green) to allow the train on yellow track to enter the junction
Physical wire
Junction’s Senor-Signal physical wire connection and operating logic

## Slide 8
Railway System Emulator [ Program workflow diagram]
Program start
Loading config files
Program system config file
Real world connector (thread1)
Logic calculator (thread2)
Ladder logic bank
Modbus server (thread3)
Real world Communication loop
Register and coils state manager
real-world input sensor data
Holding register state change data
Coils state change data
real-world output signal data
Change Coils state
Read holing register state
Modbus request queue handling loop
Network
Network
UDP data flow
2D Railway[Metro] System Real-world Emulator
Railway[Metro] System SCADA-HMI

## Slide 10
Direct trigger latching relay implemented by PLC ladder logic
Train docking sensor
Train exit station block signal light
Operation Scenario 1: Train enter the station and trigger the docking sensor:
Operation Scenario 2: Station turn on train exit signal to stop the train for docking, also turn on the station enter block signal to avoid other trains enters the station:
Train enter station block signal light
Operation Scenario 3: When the train finished docking, turn off both signal light to allow train left the station:
Station waits another train dock:
Physical wire
Station’s Senor-Signal physical wire connection and operating logic

## Slide 11
Train speed sensor
Train power (moto)
PLC input connector
PLC output connector
Operation Scenario 1(Red) : Train power off, Train speed is 0 km/ h
Operation Scenario 2(Orange) : Train power on , Train speed is low (0 km/ h – 20km/h)
Operation Scenario 2(Green) : Train power on , Train speed is normal (56 km/ h – 90 km/ h)
Train’s Senor-Power physical wire connection and operating logic

## Slide 12
Railway System Emulator [ Program workflow diagram]
Program start
Loading config files
Program system config file
Real world connector (thread1)
Modbus server (thread2)
Real world Communication loop
Register and coils state manager
real-world input sensor data
real-world output signal data
Change Coils state
Read holing register state
Modbus request queue handling loop
Network
Network
UDP data flow
2D Railway[Metro] System Real-world Emulator
Trains Control HMI

## Slide 13
Program start
Loading config files
Program system config file
Init main UI (main thread)
Init PLC Connector (sub thread )
UI data controller (map manager)
Display UI info panel
Train power control panels
Display UI refresh loop
PLC state data
Power Control event
PLC data controller (data manager)
Holding register data
Coil state change data
PLC client (Modbus TCP client)
PLC state data
Network
Trains Sensor-Power System Control PLC Simulator module
PLC state panels
Trains information
Modbus TCP data

## Slide 14
Trains information display grid
Turn train power ON button
Turn train power OFF button (emergency stop)
PLC state panel
PLC connection state
PLC coils state indicator
PLC holding register state indicator
Date & time
Critical information and error state display bar

## Slide 15
Emergency Stop button pressed (Mode-B) :
Train power off, Train totally stop[speed=0], Current cut off. Voltage range in (Normal , Max. permanent)
PLC speed sensor (Register) indicator OFF (grey).
PLC train motor power indicator OFF (white)
Train normal operation mode A-1 (docking/waiting):
Train power on, Train speed very low [<5km/h], Current drop low. Voltage range in (Min. permanent , Normal)
PLC speed sensor (Register) indicator OFF (grey).
PLC train motor power indicator ON (green)
Train normal operation mode A-2 (running)

## Slide 16
Program start
Loading config files
Program system config file
Init main UI (main thread)
Init PLC Connector (sub thread )
UI data controller (map manager)
Map display panel
PLC set 1 state display panels
Display UI refresh loop
PLC state data
PLC data controller (data manager)
Holding register data
Coil state change data
Junction PLC client (Modbus TCP client)
PLC state data
Network
Railway Junctions Sensor-Signal System Control PLC Simulator
PLC set 2 state display panels
Digital I/O Information
Modbus TCP data
Station PLC client (Modbus TCP client)
Modbus TCP data
Railway Stations Sensor-Signal System Control PLC Simulator
PLC state data
PLC state data

## Slide 17
Junction block sensor [with red dash line]
Junction block sensor [with green dash line]
Junction block signal ON [Red]
Junction block signal OFF [Green]
Junction release sensor triggered [ Yellow]
Junction block sensor triggered [ Yellow]
Train station docking sensor [Grey]
Train station docking sensor triggered [Yellow]
Train station signal [green]
PLC information
PLC coil voltage high
PLC coil voltage low
Digital input connected
Digital input empty
PLC register state voltage high
PLC register state voltage low
Digital output connected
Digital output empty

## Slide 18
Station triggered example
Step 1.0: In real-world emulator, train triggered the station docking sensor, Digital input signal change the register’s state
Step 2.0: PLC executes the ladder logic, turn on coils to change the digital output
Step 1.1 :Map station sensor changed to triggered state (yellow color)
Step 3: Real-world emulator signal turn on to block the train.
Step 2.0: Map station signal changed to block state (red color)

## Slide 19
Step 1.0: In real-world emulator, train triggered the junction entrance sensor, Digital input change the register’s state
Step 1.1: In the map the sensor will show triggered state (yellow color)
Step 2.0: PLC execute the ladder logic, then change the coil sate
Step 2.1: digital output will change the related signal connect to it to block the junction
Step 3.0: In real-world emulator, train triggered the junction release sensor, Digital input change the register’s state
Step 3.1: digital output will change the related signal connect to it to release the junction

## Slide 20
Railway Real-world Emulator VM/Node
10.0.10.100
Train Control PLC VM/VMs
10.0.10.13
Station Control PLC VM/VMs
Signal Control PLC VM/VMs
10.0.10.12
10.0.10.11
Real world electrical signal simulation subnet
Real world emulator program
PLC Simulator Program
PLC Simulator Program
PLC Simulator Program
Railway HMI program [master]
SCADA HMI Operation VM/Node
Railway HMI program
SCADA HMI Monitor VM/Node
SCADA HMI subnet
192.168.10.100
192.168.10.10X
192.168.11.10
192.168.11.1X
Train driver subnet
192.168.100.13
192.168.100.12
192.168.100.11
192.168.100.2xx
OT-Network
IT-Network
Train control program

## Slide 21
Railway real-world Emulator
Electrical signal communication simulation module (10.0.10.100)
[Master, Slot-0]
I/O: 15/7
[Slave, Slot-1]
I/O: 15/7
[Slave, Slot-2]
I/O: 9/5
39 sensors input
19 signal coils output
PLC-00
PLC-01
PLC-02
Junction Signal control PLC network
[Master, Slot-0]
I/O: 8/8
[Slave, Slot-1] I/O: 8/8
[Slave, Slot-2] I/O: 6/6
PLC-03
PLC-04
PLC-05
Station Signal control PLC network
22 station
Signal output
22 station
Sensors input
Train control PLC network [under progress ]
PLC-06
PLC-07
[Slave, Slot-1] I/O: 0/2
[Master, Slot-0]
I/O: 0/8
10 train throttle
input
10.0.13.10
10.0.12.10
10.0.11.10
Railway SCADA HMIs
Modbus Network 192.168.100.0/24
Modbus IP: 192.168.100.13
Modbus IP: 192.168.100.12
Modbus IP: 192.168.100.11
Master HMI IP: 192.168.10.100
Coils control request
Register control request
Coils control request
Register control request
Coils control request
Master HMI
Slave HMI(s)
Slave HMI IP: 192.168.10.10X
Register control
Coils control
Register data fetch
Coils data fetch
HMI network 192.16.10.x
Train Control panel
Modbus IP: 192.168.100.2xx
Coils control request
UDP data flow:
Modbus TCP data flow:

## Slide 22
Cooperate network [IT network]
Supervision network SCADA
Production network
Physical real world emulation network
Real world emulator
Track junction sensors-signals control emulators
Train station sensors-signals control emulators
Train emulators
Junction sensor-signal control PLCs set [emulator]
Station sensor-signal control PLCs set [emulator]
Train controller PLCs [emulator]
Electrical signal out
Electrical signal in
Railway system SCADA server
Trains system SCADA server
Trains monitor & control HMI
Railway monitor & control HMI
Maintenance laptops
Cooperate Network
ICS [OT network ]
Railway HQ operator
Trains driver /operator
Production management workstation
ERP servers
Cooperate IT servers
Users, staff and manager
IT management computers
IT engineer
ICS engineer
Railway[Metro] IT/OT System Security Test Platform Network Diagram and Components View
Local HW-Engineering admin laptop
Field device admin
Ethernet TCP/IP
Ethernet TCP/IP and Modbus TCP
Modbus TCP

## Slide 23
Cooperate network [IT network]
Supervision network SCADA
Production network
Physical real world emulation network
Track junction sensors-signals control emulators
Train station sensors-signals control emulators
Train emulators
Junction sensor-signal control PLCs set [emulator]
Station sensor-signal control PLCs set [emulator]
Train controller PLCs [emulator]
Electrical signal out
Electrical signal in
Railway system SCADA server
Trains system SCADA server
Trains monitor & control HMI
Railway monitor & control HMI
Maintenance laptops
Cooperate Network
ICS [OT network ]
Railway HQ operator
Trains driver /operator
Production management workstation
ERP servers
Cooperate IT servers
Users, staff and manager
IT management computers
IT engineer
ICS engineer
Railway[Metro] IT/OT System Security Test Platform Network Diagram and Components View
Local HW-Engineering admin laptop
Field device admin
Ethernet TCP/IP
Ethernet TCP/IP and Modbus TCP
Modbus TCP

## Slide 24
[Master, Slot-0]
I/O: 15/7
[Slave, Slot-1]
I/O: 15/7
[Slave, Slot-2]
I/O: 9/5
PLC-00
PLC-01
PLC-02
Junction Signal control PLC network
PLC0 Q0.0
S-we-0
PLC0 Q0.2
S-we-2
PLC0 Q0.4
S-we-4
PLC0 Q0.6
S-we-6
PLC1 Q0.0
S-we-7
PLC0 Q0.1
S-we-1
PLC0 Q0.5
S-we-5
PLC0 Q0.3
S-we-3
PLC1 Q0.1
S-ns-0
PLC1 Q0.2
S-ns-1
PLC1 Q0.3
S-ns-2
PLC1 Q0.4
S-ns-3
PLC1 Q0.5
S-cc-0
PLC1 Q0.6
S-cc-1
PLC2 Q0.0
S-cc-2
PLC2 Q0.1
S-cc-3
PLC2 Q0.2
S-cc-4
PLC2 Q0.3
S-cc-5
PLC2 Q0.4
S-cc-6
Ladder Diagram set information:
PLC number: 3
Holding register: 39
Coil: 19
Total ladder diagram: 19
Ladder diagram detail:
Railway Signal System PLC set ladder logic

## Slide 25
[Master, Slot-0]
I/O: 8/8
[Slave, Slot-1] I/O: 8/8
[Slave, Slot-2] I/O: 6/6
PLC-03
PLC-04
PLC-05
Station Signal control PLC network
10.0.12.10
Ladder Diagram set information:
PLC number 3
Holding register: 22
Coil: 22
Total ladder diagram: 22
Ladder diagram detail:
Railway Station system PLC set ladder logic

## Slide 26
Train Control PLC Configuration
Train control PLC network [under progress ]
PLC-06
PLC-07
[Slave, Slot-1] I/O: 0/2
[Master, Slot-0]
I/O: 0/8
Ladder Diagram set information:
PLC number 2
Holding register: 0
Coil: 10
Total ladder diagram: N.A (direct control)
Ladder diagram detail: N.A