## Slide 1
Train Speed Reset
Train Emergency Stop
Train Sensor
Train Station
Railway Cross Signal
Green: Pass [off]
Red: Block [on]

## Slide 2
Real work sensor data
PCL coil output data
Database
Communication manager
PCL input data
PCL coil output data
ModBus TCP
PLC simulator VM
SCADA HMI data Visualization
Metro Control HMI

## Slide 3
Signal Trigger on sensor
Signal Trigger off sensor
Railway control signal
Use PLC to create a T Flip – Flop latching relay with signal trigger on has high priority

## Slide 4
Railway System Emulator [ Program workflow diagram]
Program start
Loading config files
Program system config file
Station config file
Scenario config file
Init main UI (main thread)
Init PLC request handler (sub thread )
UI data controller (map manager)
Display UI map panel
Train power control panels
Display UI refresh loop
Components state data
Control event
PLC data controller (data manager)
Holding register data
Coil state change data
PLC Connector (UDP server)
PLC state data
Network
Other PLC modules
Other PLC modules
Other PLC modules
Use UDP to simulate the real-word electrical system wires connection
System auto controller ( if test mode )
All Plc connection and data update state

## Slide 5
Train
Scenario load drop down menu
Date and Time
Station
PLC connection state
Trains power control panels
Trains collision auto avoidance control
Train position sensors
Railway track signals

## Slide 6
Train control panel
Train power on Button
Train position reset button
Emergency Stop button (power cut off)
Train auto collision avoidance on/off control
Train auto collision avoidance OFF:
Behind train will “hit” the front stopped train directly and stop. An accident indicator will flash at the accident position
UI scenario :
Train auto collision avoidance ON:
Behind train will change speed to 0 to wait the front train if the train’s sensor detects a train in it front in the safety threshold distance.
UI scenario :
Step 1: click config dropdown menu and select “load scenario”
Step 2:When the Scenario selection window pop-up,
Click the Scenario you want to load
Step 3: Click “OK” to load to the real-world simulator

## Slide 7
Junction entrance block sensor
Junction Area
Junction entrance release sensor
T-flip-flop latching relay implemented by PLC ladder logic
Train entrance block signal
Step 1: When a train is entering the junction and trigger the entrance block sensor (sensor color change from grey to blue )
Operation Scenario 1: Junction block when train pass through
Step 2: Junction entrance block signal will turn on (red) to block the train on yellow track to enter the junction
Operation Scenario 1: Junction release when train leaving
Step 3: When a train is leaving the junction and trigger the entrance release sensor (sensor color change from grey to blue )
Step 4: Junction entrance block signal will turn OFF (green) to allow the train on yellow track to enter the junction
Physical wire
Junction’s Senor-Signal physical wire connection and operating logic

## Slide 8
Railway System Emulator [ Program workflow diagram]
Program start
Loading config files
Program system config file
Real world connector (thread1)
Logic calculator (thread2)
Ladder logic bank
Modbus server (thread3)
Real world Communication loop
Register and coils state manager
real-world input sensor data
Holding register state change data
Coils state change data
real-world output signal data
Change Coils state
Read holing register state
Modbus request queue handling loop
Network
Network
UDP data flow
2D Railway[Metro] System Real-world Emulator
Railway[Metro] System SCADA-HMI

## Slide 10
Direct trigger latching relay implemented by PLC ladder logic
Train docking sensor
Train exit station block signal light
Operation Scenario 1: Train enter the station and trigger the docking sensor:
Operation Scenario 2: Station turn on train exit signal to stop the train for docking, also turn on the station enter block signal to avoid other trains enters the station:
Train enter station block signal light
Operation Scenario 3: When the train finished docking, turn off both signal light to allow train left the station:
Station waits another train dock:
Physical wire
Station’s Senor-Signal physical wire connection and operating logic

## Slide 11
Railway Real-world Emulator VM/Node
10.0.10.100
Train Control PLC VM/VMs
10.0.10.13.10
Station Control PLC VM/VMs
Signal Control PLC VM/VMs
10.0.10.12.10
10.0.10.12.11
Real world electrical signal simulation subnet
Real world emulator program
PLC Simulator Program
PLC Simulator Program
PLC Simulator Program
Railway HMI program [master]
SCADA HMI Operation VM/Node
Railway HMI program
SCADA HMI Monitor VM/Node
SCADA HMI subnet
192.168.10.100
192.168.10.10X
192.168.11.10
192.168.11.1X
Train driver subnet
192.168.100.13
192.168.100.12
192.168.100.11
192.168.100.2xx
OT-Network
IT-Network
Train control program

## Slide 12
Railway real-world Emulator
Electrical signal communication simulation module (10.0.10.100)
[Master, Slot-0]
I/O: 15/7
[Slave, Slot-1]
I/O: 15/7
[Slave, Slot-2]
I/O: 9/5
39 sensors input
19 signal coils output
PLC-00
PLC-01
PLC-02
Junction Signal control PLC network
[Master, Slot-0]
I/O: 8/8
[Slave, Slot-1] I/O: 8/8
[Slave, Slot-2] I/O: 6/6
PLC-03
PLC-04
PLC-05
Station Signal control PLC network
22 station
Signal output
22 station
Sensors input
Train control PLC network [under progress ]
PLC-06
PLC-07
[Slave, Slot-1] I/O: 0/2
[Master, Slot-0]
I/O: 0/8
10 train throttle
input
10.0.13.10
10.0.12.10
10.0.11.10
Railway SCADA HMIs
Modbus Network 192.168.100.0/24
Modbus IP: 192.168.100.13
Modbus IP: 192.168.100.12
Modbus IP: 192.168.100.11
Master HMI IP: 192.168.10.100
Coils control request
Register control request
Coils control request
Register control request
Coils control request
Master HMI
Slave HMI(s)
Slave HMI IP: 192.168.10.10X
Register control
Coils control
Register data fetch
Coils data fetch
HMI network 192.16.10.x
Train Control panel
Modbus IP: 192.168.100.2xx
Coils control request
UDP data flow:
Modbus TCP data flow:

## Slide 13
[Master, Slot-0]
I/O: 15/7
[Slave, Slot-1]
I/O: 15/7
[Slave, Slot-2]
I/O: 9/5
PLC-00
PLC-01
PLC-02
Junction Signal control PLC network
PLC0 Q0.0
S-we-0
PLC0 Q0.2
S-we-2
PLC0 Q0.4
S-we-4
PLC0 Q0.6
S-we-6
PLC1 Q0.0
S-we-7
PLC0 Q0.1
S-we-1
PLC0 Q0.5
S-we-5
PLC0 Q0.3
S-we-3
PLC1 Q0.1
S-ns-0
PLC1 Q0.2
S-ns-1
PLC1 Q0.3
S-ns-2
PLC1 Q0.4
S-ns-3
PLC1 Q0.5
S-cc-0
PLC1 Q0.6
S-cc-1
PLC2 Q0.0
S-cc-2
PLC2 Q0.1
S-cc-3
PLC2 Q0.2
S-cc-4
PLC2 Q0.3
S-cc-5
PLC2 Q0.4
S-cc-6
Ladder Diagram set information:
PLC number: 3
Holding register: 39
Coil: 19
Total ladder diagram: 19
Ladder diagram detail:
Railway Signal System PLC set ladder logic

## Slide 14
[Master, Slot-0]
I/O: 8/8
[Slave, Slot-1] I/O: 8/8
[Slave, Slot-2] I/O: 6/6
PLC-03
PLC-04
PLC-05
Station Signal control PLC network
10.0.12.10
Ladder Diagram set information:
PLC number 3
Holding register: 22
Coil: 22
Total ladder diagram: 22
Ladder diagram detail:
Railway Station system PLC set ladder logic

## Slide 15
Train Control PLC set logic [under progress]
Train control PLC network [under progress ]
PLC-06
PLC-07
[Slave, Slot-1] I/O: 0/2
[Master, Slot-0]
I/O: 0/8
Ladder Diagram set information:
PLC number 2
Holding register: 0
Coil: 10
Total ladder diagram: N.A (direct control)
Ladder diagram detail: N.A