## Slide 1
Train Speed Reset
Train Emergency Stop
Train Sensor
Train Station
Railway Cross Signal
Green: Pass [off]
Red: Block [on]

## Slide 2
Real work sensor data
PCL coil output data
Database
Communication manager
PCL input data
PCL coil output data
ModBus TCP
PLC simulator VM
SCADA HMI data Visualization
Metro Control HMI

## Slide 3
Signal Trigger on sensor
Signal Trigger off sensor
Railway control signal
Use PLC to create a T Flip – Flop latching relay with signal trigger on has high priority

## Slide 4
Railway System Emulator [ Program workflow diagram]
Program start
Loading config files
Program system config file
Station config file
Scenario config file
Init main UI (main thread)
Init PLC request handler (sub thread )
UI data controller (map manager)
Display UI map panel
Train power control panels
Display UI refresh loop
Components state data
Control event
PLC data controller (data manager)
Holding register data
Coil state change data
PLC Connector (UDP server)
PLC state data
Network
Other PLC modules
Other PLC modules
Other PLC modules
Use UDP to simulate the real-word electrical system wires connection
System auto controller ( if test mode )
All Plc connection and data update state

## Slide 5
Train
Scenario load drop down menu
Date and Time
Station
PLC connection state
Trains power control panels
Trains collision auto avoidance control
Train position sensors
Railway track signals

## Slide 6
Train control panel
Train power on Button
Train position reset button
Emergency Stop button (power cut off)
Train auto collision avoidance on/off control
Train auto collision avoidance OFF:
Behind train will “hit” the front stopped train directly and stop. An accident indicator will flash at the accident position
UI scenario :
Train auto collision avoidance ON:
Behind train will change speed to 0 to wait the front train if the train’s sensor detects a train in it front in the safety threshold distance.
UI scenario :
Step 1: click config dropdown menu and select “load scenario”
Step 2:When the Scenario selection window pop-up,
Click the Scenario you want to load
Step 3: Click “OK” to load to the real-world simulator

## Slide 7
Railway Real-world Emulator VM/Node
10.0.10.100
Train Control PLC VM/VMs
10.0.10.13.10
Station Control PLC VM/VMs
Signal Control PLC VM/VMs
10.0.10.12.10
10.0.10.12.11
Real world electrical signal simulation subnet
Real world emulator program
PLC Simulator Program
PLC Simulator Program
PLC Simulator Program
Railway HMI program [master]
SCADA HMI Operation VM/Node
Railway HMI program
SCADA HMI Monitor VM/Node
SCADA HMI subnet
192.168.10.100
192.168.10.10X
192.168.11.10
192.168.11.1X
Train driver subnet
192.168.100.13
192.168.100.12
192.168.100.11
192.168.100.2xx
OT-Network
IT-Network
Train control program

## Slide 8
Railway real-world Emulator
Electrical signal communication simulation module (10.0.10.100)
[Master, Slot-0]
I/O: 15/7
[Slave, Slot-1]
I/O: 15/7
[Slave, Slot-2]
I/O: 9/5
39 sensors input
19 signal coils output
PLC-00
PLC-01
PLC-02
Junction Signal control PLC network
[Master, Slot-0]
I/O: 8/8
[Slave, Slot-1] I/O: 8/8
[Slave, Slot-2] I/O: 6/6
PLC-03
PLC-04
PLC-05
Station Signal control PLC network
22 station
Signal output
22 station
Sensors input
Train control PLC network [under progress ]
PLC-06
PLC-07
[Slave, Slot-1] I/O: 0/2
[Master, Slot-0]
I/O: 0/8
10 train throttle
input
10.0.13.10
10.0.12.10
10.0.11.10
Railway SCADA HMIs
Modbus Network 192.168.100.0/24
Modbus IP: 192.168.100.13
Modbus IP: 192.168.100.12
Modbus IP: 192.168.100.11
Master HMI IP: 192.168.10.100
Coils control request
Register control request
Coils control request
Register control request
Coils control request
Master HMI
Slave HMI(s)
Slave HMI IP: 192.168.10.10X
Register control
Coils control
Register data fetch
Coils data fetch
HMI network 192.16.10.x
Train Control panel
Modbus IP: 192.168.100.2xx
Coils control request
UDP data flow:
Modbus TCP data flow:

## Slide 9
[Master, Slot-0]
I/O: 15/7
[Slave, Slot-1]
I/O: 15/7
[Slave, Slot-2]
I/O: 9/5
PLC-00
PLC-01
PLC-02
Junction Signal control PLC network
PLC0 Q0.0
S-we-0
PLC0 Q0.2
S-we-2
PLC0 Q0.4
S-we-4
PLC0 Q0.6
S-we-6
PLC1 Q0.0
S-we-7
PLC0 Q0.1
S-we-1
PLC0 Q0.5
S-we-5
PLC0 Q0.3
S-we-3
PLC1 Q0.1
S-ns-0
PLC1 Q0.2
S-ns-1
PLC1 Q0.3
S-ns-2
PLC1 Q0.4
S-ns-3
PLC1 Q0.5
S-cc-0
PLC1 Q0.6
S-cc-1
PLC2 Q0.0
S-cc-2
PLC2 Q0.1
S-cc-3
PLC2 Q0.2
S-cc-4
PLC2 Q0.3
S-cc-5
PLC2 Q0.4
S-cc-6
Ladder Diagram set information:
PLC number: 3
Holding register: 39
Coil: 19
Total ladder diagram: 19
Ladder diagram detail:
Railway Signal System PLC set ladder logic

## Slide 10
[Master, Slot-0]
I/O: 8/8
[Slave, Slot-1] I/O: 8/8
[Slave, Slot-2] I/O: 6/6
PLC-03
PLC-04
PLC-05
Station Signal control PLC network
10.0.12.10
Ladder Diagram set information:
PLC number 3
Holding register: 22
Coil: 22
Total ladder diagram: 22
Ladder diagram detail:
Railway Station system PLC set ladder logic

## Slide 11
Train Control PLC set logic [under progress]
Train control PLC network [under progress ]
PLC-06
PLC-07
[Slave, Slot-1] I/O: 0/2
[Master, Slot-0]
I/O: 0/8
Ladder Diagram set information:
PLC number 2
Holding register: 0
Coil: 10
Total ladder diagram: N.A (direct control)
Ladder diagram detail: N.A